## Slide 1
EDGE AI &
MACHINE LEARNING INFERENCE
A Comprehensive Practical Guide
3–6 Hours
Duration
Windows + VS Code
Platform
YOLO + ONNX
Focus
Engineering
Level
National University of Management | National Polytechnic Institute of Cambodia · 2026
Notes: Welcome and introduce yourself. Explain the session plan: 3-6 hours covering Edge AI fundamentals through practical YOLO deployment. Ask students about their background with Python and AI.

## Slide 2
Session Agenda
3–6 hours · Practical + Theory
01
Introduction to Edge AI
30 min
⏱ 30 min
02
Theory & Architecture
40 min
⏱ 40 min
03
Environment Setup
45 min
⏱ 45 min
04
YOLO Model Deployment
60 min
⏱ 60 min
05
Advanced Applications
60 min
⏱ 60 min
06
Tracking & Analytics
50 min
⏱ 50 min
07
Projects & Assessment
45 min
⏱ 45 min
08
Future of Edge AI
30 min
⏱ 30 min
Notes: Walk through the agenda. Emphasize that labs are hands-on — students should have their computers ready. The schedule is flexible; adjust pacing based on student progress.

## Slide 3
Learning Objectives
By the end of this session, you will be able to:
LO1
Explain Edge AI principles and compare with cloud-based AI architectures
LO2
Set up a Python development environment with VS Code and virtual environments
LO3
Deploy pre-trained YOLO models for real-time object detection via webcam
LO4
Export models to ONNX format and benchmark inference performance
LO5
Build real-time applications: ROI detection, people counters, and tracking
LO6
Apply model optimization: quantization, pruning, and architecture selection
LO7
Create professional monitoring dashboards for Edge AI systems
LO8
Design and evaluate Edge AI projects for real-world deployment
Notes: Review each learning objective. Connect LO3–LO5 to the hands-on lab exercises. Encourage students to refer back to these objectives as they progress through sections.

## Slide 4
SECTION 01
Introduction to Edge AI
What Is Edge AI?
Edge AI deploys and executes AI algorithms directly on local hardware — microcontrollers, single-board computers, smartphones, and embedded systems — rather than relying on centralized cloud servers. This brings computation physically closer to the source of data.
Real-Time
Sub-50ms latency
for critical decisions
Privacy
Data stays on device
never leaves premises
Offline
Works without
internet connectivity
Key Applications:
Autonomous Vehicles
Industrial Robotics
Quality Inspection
Medical Monitoring
Smart Security
Agriculture
Notes: Define Edge AI clearly. Emphasize the shift from cloud-centric to on-device computation. Ask: 'What happens if your self-driving car loses WiFi?' This motivates why edge matters. Spend ~5 minutes on this slide.

## Slide 5
Edge AI vs. Cloud AI — Architectural Trade-Offs
Cloud AI
Edge AI
Latency
50–500+ ms (network round-trip)
1–50 ms (on-device)
Privacy
Data leaves premises to remote servers
Data stays on machine always
Bandwidth
High — raw data must be uploaded
Minimal — only metadata/alerts
Cost at Scale
Recurring API/GPU rental fees
One-time hardware investment
Model Power
Unlimited (cloud GPU clusters)
GPU/NPU-dependent
Scalability
Elastic, on-demand scaling
Per-machine deployment
✓ Edge wins for: Real-time control · Privacy-sensitive data · Remote/offline sites · Continuous high-throughput inference
Notes: Walk through each row. The key insight: Edge doesn't win everything, but for IoT and safety-critical scenarios, the latency and privacy advantages are decisive. Cloud still wins for very large models and burst workloads.

## Slide 6
Why Edge AI Matters — 4 Key Drivers
01
Latency Reduction
5–50 ms
On-Device
Cloud AI: 50–500+ ms round-trip
Critical for AV, robotics, surgery
100 ms extra latency = safety risk
02
Privacy & Data Sovereignty
0 bytes
Sent to cloud
HIPAA, GDPR, CCPA compliance
Medical images stay on device
No raw video transmitted
03
Bandwidth & Offline
1.5 Gbps
1080p raw stream
Edge sends only metadata/alerts
Works in mines, ships, rural sites
Air-gapped deployments supported
04
Cost Efficiency
$0
Per inference
No recurring API fees at scale
One-time hardware investment
Laptop = dev + deployment platform
Notes: For each driver, give a real example: Latency→autonomous emergency brake; Privacy→hospital X-ray analysis; Bandwidth→multi-camera factory floor; Cost→startup budget constraints. Allow 8-10 minutes here.
Key Drivers កត្តាជំរុញសំខាន់ៗ
HIPAA, GDPR, CCPA compliance ការអនុលោមតាម HIPAA, GDPR, CCPA

## Slide 7
Why Edge Inference Matters
Latency
<5ms
Edge inference
(on-device)
50-200ms
Cloud inference
(network round-trip)
Critical for real-time:
Autonomous driving
AR/VR pipelines
Industrial robot control
Medical monitoring
Eliminating network round-trips enables applications where milliseconds determine safety outcomes.
4 / 26

## Slide 8
Why Edge Inference Matters
Privacy & Data Sovereignty
Data never leaves the device
Biometrics, health data, conversations stay local
Regulatory compliance
GDPR, HIPAA satisfied by design
Reduced attack surface
No cloud transmission = fewer interception vectors
User trust
Consumers demand on-device processing for personal data
5 / 26

## Slide 9
Why Edge Inference Matters
Bandwidth & Connectivity
75B+
IoT devices
by 2030
2.5 EB
Daily global
data generated
40%
Unreliable
connectivity worldwide
Edge AI processes data locally, sending only results to the cloud. This dramatically reduces bandwidth requirements and enables disconnected operation.
6 / 26
Notes: 2.5 EB = 2621440 TB
Edge AI ដំណើរការទិន្នន័យនៅ locally ដោយផ្ញើតែលទ្ធផលទៅកាន់ cloud ប៉ុណ្ណោះ។ នេះកាត់បន្ថយតម្រូវការ bandwidth យ៉ាងខ្លាំង និងអាចឱ្យប្រតិបត្តិការផ្តាច់ចេញ។

## Slide 10
Why Edge Inference Matters
Cost Efficiency
Chart: 
| Compute | Bandwidth | Storage | Total
Cloud AI (annual) | 45000 | 12000 | 8000 | 65000
Edge AI (annual) | 15000 | 2000 | 3000 | 20000
Key cost benefits:
No per-inference API charges
Reduced cloud provisioning
Lower data transfer costs
One-time HW vs. recurring cloud fees
7 / 26
Notes: អត្ថប្រយោជន៍សំខាន់ៗនៃការចំណាយ៖
គ្មានការគិតថ្លៃ API ក្នុងមួយការសន្និដ្ឋាន
កាត់បន្ថយការផ្តល់សេវាកម្មលើ Cloud
កាត់បន្ថយការចំណាយលើការផ្ទេរទិន្នន័យ
ថ្លៃសេវា HW ម្តងបើប្រៀបធៀបទៅនឹងថ្លៃសេវា Cloud ដដែលៗ

## Slide 11
Common Frameworks & Deployment Tools
Framework | Vendor | Target Platform
TensorFlow Lite | Google | Mobile, embedded, microcontrollers
ONNX Runtime | Microsoft | Cross-platform, multi-framework
TensorRT | NVIDIA | GPU-optimized inference
Core ML | Apple | iOS/macOS native inference
OpenVINO | Intel | Intel CPU/GPU/VPU optimization
MediaPipe | Google | Real-time ML pipelines
Choose based on target hardware, model format, and deployment constraints.
10 / 26

## Slide 12
ML Lifecycle: Training vs. Inference
This guide focuses exclusively on the Inference phase — deploying pre-trained models to edge devices for real-time prediction.
TRAINING
Definition:
Learning model parameters from labeled data
Compute:
GPU clusters, TPU pods — extremely high
Data:
Thousands to millions of labeled samples
Location:
Cloud data centers, HPC clusters
Duration:
Hours to weeks per training run
Goal:
Maximize accuracy and generalization
Frequency:
Periodic (retrain on new data batches)
INFERENCE
Definition:
Using trained model to make predictions
Compute:
Moderate to low — runs on edge devices
Data:
Single sample or small batch at a time
Location:
Edge devices, local machines
Duration:
Milliseconds per prediction
Goal:
Minimize latency, memory, and power
Frequency:
Continuous (every sensor reading/frame)
🎯 Session Focus: Inference only — models are pre-trained; we deploy, optimize, and benchmark them on local hardware
Notes: Students often confuse training and inference. Clarify: we're NOT training models today. The model was already trained by Ultralytics on COCO dataset. We load and run it. This is edge INFERENCE. Training requires 100x more compute.

## Slide 13
The Edge AI Technology Stack
05 Integration Layer
MQTT, gRPC, REST, GPIO, USB — connects pipeline to sensors, actuators, dashboards
04 Application Layer
Orchestration: capture → preprocess → infer → post-process → visualize → alert
← Today
03 Model Layer
Pre-trained neural network: quantization, pruning, knowledge distillation applied
← Today
02 Runtime Layer
Inference engine: ONNX Runtime, TensorRT, TFLite, OpenVINO, CoreML, SNPE
← Today
01 Hardware Layer
Physical compute: CPU, GPU, NPU, TPU, FPGA, or dedicated AI accelerator chip
Notes: This stack diagram grounds everything we do today. Our focus: Runtime (ONNX), Model (YOLOv8), and Application layers. The hardware is your laptop CPU/GPU. Integration (MQTT) is covered briefly in future sessions.

## Slide 14
YOLO — You Only Look Once
The industry standard for real-time object detection at the edge — single forward pass through the network.
Single-Stage Detection
Predicts boxes AND class probabilities simultaneously in one pass — no proposal generation bottleneck
Anchor-Free (v8+)
Direct keypoint prediction — better generalization to unusual object shapes and aspect ratios
Multiple Sizes
Nano (3.2M params) to Extra-Large (68.2M params) — choose based on hardware constraints
Multi-Task Support
Detection, segmentation, pose estimation, classification, oriented bounding boxes — one API
Model Comparison
Model
Params
mAP50
CPU ms
YOLOv8n
3.2M
37.3
~80ms
★
YOLOv8s
11.2M
44.9
~130ms
YOLOv8m
25.9M
50.2
~240ms
YOLOv8l
43.7M
52.9
~400ms
YOLOv8x
68.2M
53.9
~600ms
★ We use YOLOv8n (Nano) for all lab exercises
Notes: YOLO = You Only Look Once. Key insight: two-stage detectors (Faster R-CNN) first find regions then classify. YOLO does both in one pass. This is why it's fast enough for real-time edge use. YOLOv8n has only 3.2M parameters — tiny enough for embedded devices.

## Slide 15
SECTION 02 — Environment Setup
01
Install Python 3.11
python.org/downloads → Python 3.11.x 64-bit
CHECK ✓ 'Add python.exe to PATH'
Verify: python --version → Python 3.11.x
⚠ Do NOT use Python 3.12+ (package compatibility issues)
02
Install VS Code
code.visualstudio.com → latest stable
Check 'Add to PATH' during install
Install Python extension (ms-python.python)
⚠ Also install Pylance, Jupyter, GitLens extensions
03
Create Virtual Environment
mkdir edge-ai-project && cd edge-ai-project
python -m venv venv
.\venv\Scripts\Activate.ps1 (PowerShell)
⚠ If error: Set-ExecutionPolicy RemoteSigned -Scope CurrentUser
04
Install Dependencies
pip install ultralytics opencv-python numpy
pip install torch onnxruntime matplotlib psutil
pip install -r requirements.txt
⚠ GPU users: pip install onnxruntime-gpu (then test with nvidia-smi)
Notes: LAB TIME: Have students follow steps 01-04. Common issues: PATH not set (Python), PowerShell execution policy, GPU vs CPU PyTorch. Walk around and help. Allow 45 minutes. Students should get all 4 verification scripts passing.

## Slide 16
Environment Verification — 4 Tests
Step 1
gpu_test.py
PyTorch & GPU check
import torch
print(torch.__version__)
print(torch.cuda.is_available())
✓ Expected: PyTorch version: 2.x.x
CUDA available: True (or False)
Step 2
nvidia-smi
NVIDIA driver check
nvidia-smi
✓ Expected: GPU table with name, driver, CUDA version
→ 'not recognized' = no GPU (use CPU mode)
Step 3
test_opencv.py
OpenCV & webcam check
import cv2
print(cv2.__version__)
cap = cv2.VideoCapture(0)
if cap.isOpened(): print('Webcam OK')
✓ Expected: OpenCV version: 4.x.x
Webcam OK — Frame size: 640x480
Step 4
test_yolo.py
YOLO model check
from ultralytics import YOLO
model = YOLO('yolov8n.pt')
print(f'{len(model.names)} classes')
✓ Expected: Model loaded: 80 classes
Inference OK — 0 detections on noise
Notes: All 4 tests must pass before moving on. If CUDA shows False — that's OK, CPU mode works for learning. If webcam fails, check camera index 0 vs 1. If YOLO model download fails, check internet connection.

## Slide 17
SECTION 03 — YOLO Model Deployment
LAB 6.1 Model Exploration
File: lab_6_1_model_info.py
from ultralytics import YOLO
model = YOLO('yolov8n.pt')
params = sum(p.numel() for p in
model.model.parameters())
print(f'Classes: {len(model.names)}')
print(f'Params: {params:,}')
✓ 80 classes · 3,157,200 total parameters · YOLOv8n on COCO 2017
LAB 6.2 Real-Time Webcam Detection
File: lab_6_2_webcam_detection.py
cap = cv2.VideoCapture(0, cv2.CAP_DSHOW)
cap.set(cv2.CAP_PROP_FRAME_WIDTH, 1280)
while True:
ret, frame = cap.read()
results = model(frame, conf=0.5)
annotated = results[0].plot()
cv2.imshow('Detection', annotated)
if cv2.waitKey(1) & 0xFF == ord('q'):
break
✓ Live annotated window · FPS counter · Press Q to quit
Neural Network Inference Pipeline
1
Input
Acquisition
→
2
Pre-
processing
→
3
Model
Loading
→
4
Forward
Pass
→
5
Post-
processing
→
6
Action /
Output
💡 Troubleshooting Tips:
Black screen → try camera index 1 or 2. | Slow FPS → reduce frame resolution or confidence threshold. | Camera busy → close Zoom/Teams/OBS before running.
Notes: LAB 6.1: Students run model_info script — confirm 80 classes and 3.1M parameters. LAB 6.2: Webcam detection — this is the exciting moment! Students see real-time detection on their own webcam. Allow 20-25 minutes. Common issue: cv2.CAP_DSHOW vs no flag — try both if camera fails.

## Slide 18
ONNX Export & Performance Benchmarking
What is ONNX?
Runtime optimization: operator fusion, constant folding, memory planning
Cross-platform: Windows, Linux, macOS, Android, iOS — one file
Hardware acceleration: CUDA, TensorRT, DirectML, OpenVINO, CoreML
Small footprint: ~50 MB runtime vs ~2 GB full PyTorch
Lab 6.3 — Export to ONNX
model = YOLO('yolov8n.pt')
export_path = model.export(
format='onnx',
imgsz=640,
simplify=True,
opset=17,
dynamic=False
)
Lab 6.5 — Benchmark Results (CPU Example)
Chart: 
| Avg Latency (ms) | FPS | RAM (MB)
PyTorch (.pt) | 46.46 | 21.52 | 415.9
ONNX Runtime | 36.91 | 27.09 | 509.3
ONNX: 20% faster latency · 26% higher FPS · works without PyTorch on deployment device
Discussion Questions
Q1: .pt vs .onnx — what's stored differently? Q4: Deploy to Raspberry Pi: PyTorch or ONNX? Q5: Why discard first 10 warm-up runs?
Notes: Key insight for students: ONNX Runtime applies graph-level optimizations the original PyTorch framework doesn't. Export once, run anywhere. For Raspberry Pi: ONNX Runtime has an ARM build (~50MB) while PyTorch ARM is ~2GB. The warm-up discards JIT compilation overhead.

## Slide 19
Model Optimization for Edge Deployment
Quantization
Reduce numerical precision
FP32 → FP16
50% size reduction, <1% accuracy loss. Default GPU start
FP16 → INT8
75% reduction, 2–4× speedup. Needs 100–1000 calibration images
Dynamic Quant
No calibration needed. Smaller speedup than static INT8
Pruning
Remove redundant weights
Structured
Remove whole filters/layers. Reduces FLOPs directly
Unstructured
Zero individual weights. Needs sparse hardware for speedup
Global Mag.
Remove lowest-magnitude weights globally across all layers
Knowledge Distillation
Teacher → Student transfer
Soft Labels
Student learns from teacher's probability distribution (dark knowledge)
Feature Mimic
Match intermediate activations, not just final output logits
Result
Compact student outperforms same-arch model trained from scratch
Architecture Selection
Pick edge-optimized models
MobileNetV3
Depthwise separable convolutions. Ideal for mobile CPU inference
EfficientNet-Lite
NAS-optimized scaling. Best accuracy-per-FLOP on constrained devices
YOLO Nano
3.2M params, 6.2 MB — runs at 30+ FPS on a laptop CPU
Notes: The most impactful optimization is often architecture selection — choose YOLO Nano over YOLO Large. Quantization FP16 is almost always safe. INT8 needs calibration data. Pruning is complex; skip for this session. Knowledge distillation is for when you need a smaller custom model.

## Slide 20
SECTION 04 — Advanced Real-Time Applications
LAB 7.1 Interactive ROI Detection
Draw ROI rectangle with mouse click-drag
Only count/detect objects inside ROI
Live dashboard: FPS, confidence, object count
Display ROI size and area in real-time
Class statistics panel (person: 3, chair: 1…)
Save snapshots with S key
CSV logging of all detections with timestamp
Adjustable confidence: UP/DOWN arrow keys
Keyboard Controls
Mouse drag: Draw ROI
R: Reset ROI
S: Save snapshot
↑/↓: Confidence ±0.05
Q: Quit
LAB 7.3 People Counter with Alert
ALERT_THRESHOLD = 3 # Max people
TARGET_CLASS = 0 # person
model = YOLO('yolov8n.pt')
cap = cv2.VideoCapture(0, cv2.CAP_DSHOW)
while True:
results = model(frame, conf=0.5)
count = sum(1 for b in results[0].boxes
if int(b.cls[0]) == TARGET_CLASS)
alert = count > ALERT_THRESHOLD
status = 'ALERT: OVER CAPACITY'
if alert:
cv2.rectangle(frame, (0,0), ..., RED, 8)
Normal: count ≤ threshold · green border · status OK
OVER CAPACITY: count > threshold · red flash border · alert text
🏭 Production Use Cases
Retail occupancy · warehouse safety zones · clean room limits · MQTT alert triggers · PLC relay activation
Notes: LAB 7.1: Interactive ROI is the most impressive demo. Students draw zones with the mouse — very visual. LAB 7.3: People counter is simpler but more production-realistic. Discuss: what happens when an alert fires in a real factory? MQTT → PLC relay → light/alarm/conveyor stop.

## Slide 21
SECTION 05 — Object Tracking & Video Analytics
Detection vs. Tracking — Key Differences
Capability
Detection Only
Detection + Tracking
Per-frame objects
✓ Bounding boxes + class labels
✓ Plus persistent unique ID per object
Identity across time
✗ Same object = new box each frame
✓ Object keeps ID until it leaves scene
Unique counting
✗ Unreliable — counts same object repeatedly
✓ Accurate — each object counted once
Path / trajectory
✗ Not possible
✓ Records position history per ID
Dwell time
✗ Not possible
✓ First-seen to last-seen timestamp
LAB 8.1 Real-Time Multi-Object Tracking
results = model.track(frame,
persist=True,
conf=0.5)
# Draw trails
for box, tid in zip(boxes, ids):
track_history[tid].append(cx, cy)
cv2.line(frame, pts[i-1], pts[i],
(0, alpha, 255), 2)
LAB 8.2 Bidirectional Line-Crossing Counter
LINE_Y = frame.shape[0] // 2
OFFSET = 30
if prev_y < LINE_Y - OFFSET
and curr_y >= LINE_Y - OFFSET:
count_down += 1
counted_ids.add(tid)
cv2.line(frame, (0, LINE_Y),
(w, LINE_Y), YELLOW, 3)
Notes: BoT-SORT = combination of Kalman filter (motion) + Re-ID features (appearance) + IoU association. Key: model.track() with persist=True maintains tracker state across frames. For line-crossing: use Y-coordinate thresholds with an offset zone to avoid double-counting at the boundary.

## Slide 22
SECTION 06 — Professional Dashboard Development
Why Dashboards Matter
Operators, engineers, and managers need real-time performance metrics, detection statistics, and system health in an intuitive visual format — transforming raw telemetry into actionable insight.
Live Video Panel
Annotated camera feed with real-time bounding boxes and class labels
Performance Metrics
FPS, latency histogram, CPU gauge, RAM utilization bars
Detection Statistics
Per-class counts, confidence distribution, objects-over-time chart
System Health Panel
GPU temp, memory pressure, disk usage, uptime, alert indicators
Lab 9.1 — Progress Bar Helper
def draw_bar(canvas, x, y, w, h,
value, max_val, color, label):
fill_w = int(w * min(value/max_val, 1.0))
cv2.rectangle(canvas, (x,y), (x+w,y+h),
DARK_BG, -1) # background
cv2.rectangle(canvas, (x,y), (x+fill_w,y+h),
color, -1) # fill
cv2.putText(canvas, f'{label}: {value:.1f}',
(x, y-5), FONT, 0.45, LIGHT, 1)
Dashboard Design Best Practices
Update Rate: smooth FPS with 5–10 frame moving average
Color Coding: green=normal, yellow=warning, red=critical
Information Hierarchy: critical info at top (FPS, alerts)
Dark Theme: standard for control rooms, reduces eye strain
Responsive Layout: relative positioning for any resolution
Notes: LAB 9.1: Students build a dual-panel dashboard — left is camera feed, right is metrics panel. The draw_bar() helper is reusable. Encourage students to add a third panel. Extension: Flask API endpoint + Chart.js frontend for remote monitoring — mention for advanced students.

## Slide 23
SECTION 07 — Capstone Deployment Projects
Complete at least 2 of 3 projects. Each integrates multiple techniques into a portfolio-ready application.
01
Intermediate
Smart Parking Occupancy Monitor
Monitor a parking area, count vehicles, display occupancy with color-coded status, log to CSV
Requirements:
Detect car/truck/motorcycle/bus in defined ROI
Color-coded status: green/yellow/red by % full
Log occupancy every 5 seconds to CSV
Side panel: count, capacity, utilization %
Skills used:
ROI filtering (Lab 7.1) · Class counting (Lab 7.3) · CSV logging · OpenCV panels
02
Intermediate
Industrial PPE Safety Inspector
Detect workers, verify hard hat compliance, alert on violations, generate audit-ready CSV report
Requirements:
Detect 'person' class (class 0)
Check upper-body region for helmet overlap
Green/red border for compliant/non-compliant
Log violations to violations/ directory
Skills used:
Detection pipeline · Bounding box geometry · Alert system · Session reports
03
Advanced
Retail Customer Flow Analytics
Track shoppers, count entries/exits via line-crossing, measure dwell time, generate analytics report
Requirements:
YOLO tracking with persistent IDs
Bidirectional line-crossing counter
Dwell time per unique ID (first/last seen)
Post-session CSV + matplotlib histogram PNG
Skills used:
model.track() (Lab 8.1) · Line crossing (Lab 8.2) · Dwell analysis · Matplotlib charts
Notes: Students should begin with Project 1 or 2 (Intermediate). Project 3 extends Lab 8 significantly. Assessment rubric: Functionality 40%, Code Quality 20%, Performance Analysis 20%, Report 20%. Allow students to present their project results if time permits.

## Slide 24
SECTION 08 — Emerging & Future Edge AI
Neural Processing Units (NPUs)
Now → 2027
Intel Meteor Lake, AMD Ryzen AI, Apple Neural Engine, Qualcomm Hexagon — 10–45 TOPS at 5–15 watts. Every laptop by 2027 will have built-in AI acceleration for YOLO-class models at 30+ FPS.
TinyML
Production now
Neural networks on microcontrollers with 256 KB RAM. TensorFlow Lite Micro, Edge Impulse, Apache TVM. Hearing aids, smart sensors, predictive maintenance, agriculture monitoring — under $5 hardware.
Federated Learning at the Edge
Pilot → 2026
Train across many devices without centralizing data. Each device shares only weight gradients. Preserves privacy, reduces bandwidth. Google Gboard and Apple Siri use this today in production.
On-Device LLMs
Expanding 2025–2027
Llama 3 (8B) running on 8 GB RAM laptops via 4-bit quantization (GPTQ, AWQ). Private AI assistants, offline document analysis, code completion — no cloud needed. Maturing fast.
Notes: Exciting discussion: ask students where they see Edge AI going in 5 years. NPUs in laptops are happening NOW — Intel AI PC certification. TinyML is real — show Edge Impulse demo if time. Federated learning is why Siri gets smarter without your data leaving your phone.

## Slide 25
Quick Reference — Commands & Resources
Environment Commands
python -m venv venv
.\venv\Scripts\Activate.ps1
pip install -r requirements.txt
pip install torch torchvision --index-url ...
pip install onnxruntime-gpu
Verification Scripts
python gpu_test.py
nvidia-smi
python test_opencv.py
python test_yolo.py
python lab_6_1_model_info.py
YOLO Key APIs
model = YOLO('yolov8n.pt')
results = model(frame, conf=0.5)
results = model.track(frame, persist=True)
model.export(format='onnx', imgsz=640)
session = ort.InferenceSession('model.onnx')
Reference Documentation
Ultralytics YOLOv8 Docs
docs.ultralytics.com
OpenCV Python
docs.opencv.org
ONNX Runtime
onnxruntime.ai/docs
PyTorch
pytorch.org/docs
NVIDIA TensorRT
developer.nvidia.com/tensorrt
Edge Impulse (TinyML)
docs.edgeimpulse.com
Notes: Keep this slide visible as a desktop reference during lab time. Students can refer to it for exact commands. Also mention the books: 'AI at the Edge' by Daniel Situnayake (O'Reilly, 2023) and 'TinyML' by Pete Warden (O'Reilly, 2020).

## Slide 26
Session Complete
You can now independently design, build, deploy, benchmark, and optimize a production-grade Edge AI inference pipeline on a standard Windows workstation — with zero cloud dependencies.
— Session Competency Target
Key Takeaways
Edge AI runs inference on local hardware — no cloud required
YOLOv8n delivers real-time detection at 20–30 FPS on CPU alone
ONNX Runtime: lighter, faster, cross-platform inference engine
FP16 quantization: 50% size reduction, <1% accuracy loss
model.track() adds persistent IDs for counting and analytics
NPUs in every laptop by 2027 — Edge AI is the career frontier
National University of Management / National Polytechnic Institute of Cambodia · 2026
Notes: Closing slide. Summarize the journey: from understanding what Edge AI is, through setting up the environment, running YOLO, optimizing with ONNX, building advanced apps, to designing real projects. Next steps: complete the capstone project, explore TinyML on a Raspberry Pi, and follow CVPR / NeurIPS papers.